## Slide 1: Solar Resource Data and Digital Tools for Renewable Energy Scale-Up
Marcel Suri
CEO, Solargis
Scaling Up Renewable Energy in Europe and Central Asia
May 26-28, 2026, Vienna, Austria, World Bank Group

## Slide 2: Table of contents
Solar data and tools used in solar energy
1. Building inventory and finding the best locations
2. Supporting large-scale PV development sites
3. Managing large fleets of solar

## Slide 3: Solar data and tools used in solar energy

## Slide 4
Solar PV in the region today

## Slide 5
Solar PV in the region today

## Slide 6
Typical utility-scale project: Hybrid PV + storage
Development and operation of solar projects strongly depends on meteorological data
Data
Solar resource: primary data for development and management
Meteorological: temperature, wind, snow, pollution affect performance
Software tools
Development: energy design, simulation, grid and revenue modelling
Operation: performance evaluation, solar power forecast
Variable renewable energy generation
Source: Adobe stock

## Slide 7
Typical utility-scale project: Hybrid PV + storage
Development and operation of solar projects strongly depends on meteorological data
Data
Solar resource: primary data for development and grid management
Meteorological: temperature, wind, snow, pollution affect performance
Software tools
Development: energy design, simulation, grid and revenue modelling
Operation: performance evaluation, solar power forecast
Variable renewable energy generation

## Slide 8
Data for solar projects needs to be available for any location in the same quality
Therefore, it is computed by models using three data inputs:
Geostationary satellite data
Global meteorological models
Meteorological ground measurements
How solar database is developed

## Slide 9
Inventory of the country’s solar potential and risks
Aggregated historical data and maps to find the best locations
Project development: Optimization of technical design and a financial plan
Detailed and accurate historical time series data (30+ years)
Monitoring of technical and financial performance of projects
Data for recent history (last months)
Solar power forecast to integrate large fleet of PV into electricity grids
Solar forecast data (up to next 14 days)
Use of solar and meteo data across project lifecycle

## Slide 10
Inventory of the country’s solar potential and risks
Aggregated historical data and maps to find the best locations
Project development: Optimization of technical design and a financial plan
Detailed and accurate historical time series data (30+ years)
Monitoring of technical and financial performance of projects
Data for recent history (last months)
Solar power forecast to integrate large fleet of PV into electricity grids
Solar forecast data (up to next 14 days)
Use of solar and meteo data across project lifecycle

## Slide 11
To make solar data accurate, to attract investment, the models need to be calibrated by ground measurements
Year 2010: Limited number of good measurements across the world (approx. 106 sites)
Solar models: Reduced uncertainty by ground measurements

## Slide 12
To make solar data accurate, to attract investment, the models need to be calibrated by ground measurements
Year 2026: Measurement campaigns in South Africa, India, Chile, Morocco, Saudi Arabia
World Bank initiatives in Pakistan, Nepal, Vietnam, West/East Africa, Pacific
Solar models: Reduced uncertainty by ground measurements
Ground measurement
campaign in West Africa:
Yearly GHI model uncertainty
reduced from 6-9% to 4-5%

## Slide 13
To make solar data accurate, to attract investment, the models need to be calibrated by ground measurements
Year 2026: Public solar measurements in Balkan, Caucasus, Turkey and Central Asia missing
Missing solar measurements

## Slide 14: Topic 1 Building inventory and finding best locations for solar

## Slide 15
World is well-mapped through private and public initiatives but with different level of uncertainty
Global Solar Atlas: open-access to global solar potential data https://globalsolaratlas.info/
Global Solar Atlas

## Slide 16: Topic 2 Supporting large-scale PV development sites

## Slide 17
Land
Permits
Grid infrastructure
…
Procuring solar measurements for the project site and more accurate solar model data
  Combining solar measurements with model reduces data uncertainty
Preparing sites for large utility-scale projects
https://solargis.com/resources/ebooks/best-practices-performance-evaluation-pv-plants

## Slide 18
1. Local meteorological measurements
  Measurements for the site: minimum 12 months
  Technical setup and deliverables are standardized
2. Data from models
  History up to 30 years
  Adapting solar models by local measurements for higher accuracy
  Delivery: high-accuracy time series and Typical Meteorological Year data
  Accurate data are distributed to all bidders
Acquiring high accuracy solar data

## Slide 19
Objective of combining measurement with models is to reduce data uncertainty
Sources of solar data uncertainty
Solar measurements and models
Solar resource variability
Climate change and long term trends
Uncertainty of solar resource
12 months of measurements reduces model uncertainty
GHI from 4-9 to 4-6%
DNI from 8-16 to 5-8%
The longer the measurements, the lower the uncertainty of the solar model

## Slide 20: From uncertainty to probability of exceedance
Uncertainty = P50 - P90
P50: Average yield — best estimate, 50% probability of exceedance, baseline
P75: 75% probability of exceedance
P90: Key lender metric — yield exceeded 90% of time
Low uncertainty
High uncertainty
Notes: Ground measurements are the reference for site adaptation. And a site adaptation is only going be as good as the reference. The uncertainty associated with the measured data has to be lower than the uncertainty of the satellite model data, to achieve any improvement.
In general, the rule is that the longer the ground measurements, the lower the achievable uncertainty after site adaptation. One full year is a minimum, but 2 to 3 years will likely improve the site adaption results.
Note here that well-installed and maintained instruments still have measurement uncertainty approaching 3%, so this is the physical limit of how good we can get. If somebody tells you their data have 1% uncertainty, you should be skeptical.
To get to this limit, the measurement campaign has to be well designed and executed. We have a handy reference for this – a new white paper published just last week, which you can find on our website in the resources section.

## Slide 21
Reducing uncertainty in solar data and energy yield calculations narrows the gap between ‘expected’ and ‘bankable’
  More accurate P50
  Higher P90
Benefits of reduced uncertainty
  Engineers: Design optimized to local geography
  Banks: Higher loan, better DSCR, lower guarantees
  Investors: Defensible base case, realistic risk assumptions, capital structure more efficient
Benefits of reduced data uncertainty
Risks are lower and better understood Higher confidence in calculation

## Slide 22: Topic 3 Management of large fleets of solar

## Slide 23: Solar variability and how to manage it
Solar resource variability
  Seasonal variability
  Day-by-day variability
  Short term variability and high frequency changes
Historical data provide insights for design of PV systems, financing, managing the risks
Solar power operation needs forecast for next minutes, hours, days
  Technical management and trading
  Managing single system or entire portfolio

## Slide 24: Solar variability and how to manage it
Solar resource variability
  Seasonal variability
  Day-by-day variability
  Short term variability and high frequency changes
Historical data provide insights for design of PV systems, financing, managing the risks
Solar power operation needs forecast for next minutes, hours days
  Technical management and trading
  Managing single system or entire portfolio

## Slide 25: Solar forecasting approaches
Standard (raw) forecast
  Global numerical weather prediction (NWP) models up to 14 days
  Nowcasting satellite model up to 4 hours
Smart forecast = accuracy enhanced by:
  Data monitored at power plants
  Price forecast (demand/supply)
  Grid operation forecast (curtailment)

## Slide 26
1 location
Forecasting accuracy for 1 site vs portfolio (Spain)

## Slide 27
49 locations
Forecasting accuracy for 1 site vs portfolio (Spain)

## Slide 28
196 locations
Forecasting accuracy for 1 site vs portfolio (Spain)

## Slide 29
Solar forecast accuracy (Slovakia)
Day ahead PV power forecast (D1)
Jan Apr Jul Oct Dec
Satellite-based PVOUT (reference)
PV power forecast - hour ahead (H1)
PV power forecast - day ahead (D1)
Forecast error
Occurrence of snow
Total considered PV capacity: 530 MW

## Slide 30
Solar forecast accuracy (Slovakia)
Day ahead forecast (D1)
Satellite-based PVOUT (reference)
PV power forecast - hour ahead (H1)
PV power forecast - day ahead (D1)
Reference Hour ahead forecast (H1) Day ahead forecast (D1)
Total considered PV capacity: 530 MW

## Slide 31
682 utility-scale PV projects: 16.48 GW
359 wind parks: 13.78 GW
Source: IFS forecast, https://globalenergymonitor.org/
Typical solar and wind generation profiles:
July
January
Complementarity of solar and wind power (Türkiye)

## Slide 32
682 utility-scale PV projects: 16.48 GW
359 wind parks: 13.78 GW
Source: IFS forecast, https://globalenergymonitor.org/
Solar and wind generation profiles in January
Low
Median
High
Complementarity of solar and wind power (Türkiye)

## Slide 33
Wind and solar are not correlated
Complementarity of solar and wind power (Türkiye)
Typical power generation profiles for solar, wind and combined

## Slide 34
Models are the only reliable data source
Data from models to be combined with on-site measurements
Once projects are online, forecast is to manage variability
  Country-wide inventory, understanding resource potential and variability
  Supporting strategical projects with site-specific measurements
    First measurements from public funding
    Later, private industry takes over
  Solar power forecasting to balance demand and supply
    Complementary profiles of solar and wind
Conclusions
Solar resource data and digital tools help to build and manage solar energy programs at the level of individual projects and entire countries

## Slide 35: Thank you
Solar Resource Data and Digital Tools for Renewable Energy Scale-Up
Marcel Suri
CEO, Solargis solargis.com

## Slide 36
Solar PV mapping and development plan (Indonesia)
Analysis of potential locations for development of 1 GW solar infrastructure in Java, Madura & Bali
Client: Southeast Asia Energy Transition Partnership (ETP) / UNOPS
Partner: Ministry of National Development Planning of Indonesia (BAPPENAS)
Implementing partner: Trama TecnoAmbiental (TTA)
Solargis provided the solar resource modelling and geospatial analysis for the project
Objectives
Site identification — technically viable areas for utility-scale PV
Environmental & social assessment — risks to ensure sustainable and responsible development
Grid impact evaluation — grid integration requirements and the hosting capacity
Site prioritization — ranked list of sites for planning utility-scale PV projects
https://www.energytransitionpartnership.org/projects/1-gw-solar-mapping-and-development-plan/
https://www.iea.org/countries/indonesia/electricity

## Slide 37
Multi-criteria geospatial analysis for selection of utility-scale PV sites
General understanding of solar resource
Grid connection, proximity to demand centres
Management of variability in PV power generation
Risk assessment
Areas where solar investment delivers the best value
Planning of future grid development
Solar PV mapping and development plan (Indonesia)